## Slide 2
Agenda
Who are we and what is PhilTel?
What’s a payphone, what’s a COCOT?
NIPCAQ Updates (Mapping and scanning payphones)
  The state of payphones in 2024
Let’s make a COCOT work
  Can we create a free-to-use programming line?
  Future Plans

## Slide 3
Who are You?
Mike
Software engineer by trade, more excited when he can use a soldering iron
Has been doing weird VoIP stuff for 12 years
Loves phreak and hacker history
Isn’t afraid to run a half-dozen modems in his basement 24/7 (Dialup.world)
Naveen
Computer engineer with IT background
Phone phreak
“That guy” calling payphones with modems
Asterisk/DAHDI/C developer
Environmental activist

## Slide 4
PhilTel
PhilTel is inspired by Futel, based out of Portland, Oregon
Bring payphones back but make them free-to-use this time (yes, we know it is a misnomer) because payphones are cool
Also focus on payphone preservation, archelogy, history, exhibition
Use as much discarded and second-hand stuff as we can, build with COTS hardware and open-source software -- nothing goes to waste!

## Slide 5
What is a Payphone?

## Slide 6
What is a COCOT?
Customer-Owned Coin-Operated Telephone
  Typically not owned by a telephone company but instead third-parties or individuals!
  Starting in the ‘80s, anyone could run their own payphones and collect the tolls for themselves
  COCOTs use “Smart boards” that rate calls at the phone itself instead of centrally at the telephone company via a coin line
  If you use a payphone in the wild these days, it is almost certainly a COCOT

## Slide 7
What is a COCOT?

## Slide 8
Where Can You Find A Payphone?
https://phreaknet.org/payphones/

## Slide 9
Philly Payphones

## Slide 10
Local Payphones

## Slide 11
What Happens If You Call A Payphone?
Historically… what you’d expect
  No charge for answering incoming calls
  Bell System had policies to prevent fraud
COCOTs typically answer with a 300/1200 baud modem
  Allows for remote management
  Useful for reporting…

## Slide 12
Protel Printouts
TC!*2152229996*72765*DD8822*4868*025*2210301004552*67805*
Number
(215)
222-9996
Amount in
Coin Box
$727.65
-$678.05
= $49.60
Model No.
Checksum
Only changes when emptied…
but not every time
% Full
= 25%
Local Timestamp
2022
October 30
00:45 local time
(12:45 am EDT)
Balance When Last Emptied
$678.05

## Slide 13
Automating It…
Usage summaries posted monthly in the NIPCAQ
https://phreakscan.com

## Slide 14
Payphone Revenue

## Slide 15
Suburban Station
Location | FW | Avg | Total | To Date | Cur Bal | Last Query | LastChg | HH:MM Ago | Total Queries | Empties
Suburban Station NE | DD8822 | $0.46 | $729.10 | $775.25 | $25.85 | 2024-02-19 00:47 | $10.05 | 535:31 | 86 | 11
Suburban Station NW | DD8822 | $0.62 | $1126.65 | $1507.75 | $16.00 | 2024-10-05 07:44 | $15.50 | 141:45 | 126 | 18
Suburban Station SE #1 | DD8822 | $0.73 | $1332.65 | $2073.10 | $35.85 | 2024-10-05 08:27 | $5.50 | 168:01 | 132 | 28
Suburban Station SE #2 | DD8432 | $1.83 | $3326.45 | $4126.30 | $53.90 | 2024-10-05 07:55 | $10.05 | 168:00 | 126 | 18

## Slide 16
Suburban Station… then and now

## Slide 17
ANACs
Identify the calling line
(800) 444-4444 – MCI
(800) 437-7950 – MCI
(844) 700-0431 – Payphone Reporting Line
Email payphones@phreaknet.org with the number and location

## Slide 18
What does this mean for hobbyists?
Many payphones on the used market these days are COCOTs
COCOTs are somewhat undesirable to collectors because they are difficult to set up
  Some COCOTs can be hand-programmed via the keypad but others require the phone to be interfaced with a PC running proprietary software
  There are many COCOT manufacturers, but the “big four” are Protel, ElcoTel, Intellicall, and Ernest, with Protel arguably being the most common/popular

## Slide 19
My Protel payphone, let’s program it!
Purchased when I was a teenager
Removed the Protel board to replace with a coinless board, but the original intention was to always use the Protel

## Slide 20
Protel Considerations
Uses NiCd battery for board power and 1/2AA Lithium battery for saving programming
Has socketed ROM (nice)
Connectors for keypad/handset, relay, coin scanner, telephone line
Programming Urban Legends:
  Need a proprietary modem to program some models (what!?)
  Need copper lines, no VoIP
  Cannot run programming software in a VM, need bare metal

## Slide 21
ExpressNet (Xnet)
‘90s DOS software to program Protel payphones remotely
Version 1.55 was cracked ages ago when someone found out a freely-downloadable upgrade disk image could become an installer
We’re going to use Windows 98 SE
  It’s familiar
  Windows 98 will be useful for other payphone software
We need an Options Record, Costing Record, and Site Record
Thanks to Dan C, John Porter, Peter (telesfor.org/payphones/), and El Jefe, wherever you are

## Slide 22
XNet Programming – Options Record

## Slide 23
XNet Programming – Costing Record

## Slide 24
XNet Programming – Costing Record

## Slide 25
XNet Programming – Costing Record (Contd)

## Slide 26
XNet Programming – Site Record

## Slide 27
Where to run XNet? Let’s use a thin client!
Virtualization can work, but not reliably (we have more to test!)
We want bare metal, but vintage hardware might not like running 24/7
Wyse V90LE!
  Low power, passive cooling, no moving parts (DOM)
  VIA C7 Eden CPU, native x86
  Real Serial port!
  Supports USB

## Slide 28
The UPMS-1200 Modem
Do we need a proprietary modem?
  Naveen called Protel, they said “No”
Protel 7000 boards need a UPMS for 1200 baud programming because they use PSK modulation instead of FSK modulation, but work fine at 300 baud otherwise
Work has been done recently to test other modems with XNet with varying results (thanks Peter!) but I cannot get them to work myself
  Your mileage may vary

## Slide 29
The UPMS-1200 Modem (Continued)
Was able to get one on eBay (eventually 2)
Was DOA 
  Replaced capacitors and relay, now it works great!
  Also added a speaker on/off switch, couldn’t mute in software

## Slide 30
How to connect the modem and the phone?
Analog PBXs and phone line simulators should work just fine, but they’re not great for public connecting
Analog Telephone Adapters won’t work (at least on both sides)
  This isn’t a problem for dial-up Internet, I can get reliable V.34 connection with ATAs for dialup.world
What else is there?

## Slide 31
Channel Bank – Adit 600
A device that muxes/demuxes a group of communications channels
Many are modular, allowing different cards for different uses
In this case, analog telephone lines are combined into a DS1 circuit going over one cable (trunk line)
Provides us a serial port for programming, T1 port, and RJ-21 (25-pair) port for phone lines
(Analog card should also work)

## Slide 32
T1/E1 Card – Sangoma A101(ish)
Adds a T1/E1 interface to your computer
Integrates with Asterisk using Digium Asterisk Hardware Device Interface (DAHDI)
Requires compiling Asterisk with DAHDI support
I have a Sangoma card, which meant using “Wanpipe” software that sits between DAHDI and the card to simulate a Digium card
If you’re doing this, just find a Digium card

## Slide 33
The PBX – Thinkstation E32 with Asterisk
Cheap SFF PC
Booting Debian 12 11
  Many issues compiling WanPipe with Debian 12, Sangoma support said use Debian 11 (sure)
  Still had issues with Debian 11, had issues with Osmocom’s alternate installation
  Found an issue with build script, submitted my fix to Sangoma, eventually it was patched
Use PhreakScript to install Asterisk, DAHDI, and Wanpipe automatically

## Slide 34
How do we program?
Hold down the program button and take the phone off-hook, hear a single beep, then release the program button
On the keypad, dial 005555555555*, you should then hear a single beep.
Next, dial 25<MODEM#>*, you should then hear a single beep.
Finally, dial *#3

## Slide 35
Success!

## Slide 36
Outcome
We have a free-to-use programming line that will rate all calls free
How can we access it?
  Via PSTN, 225-2PROTEL or 225-277-6835
  Via PhreakNet, 263-0500
  Via SIP, protel:protel@programming.philtel.org:16556
We take custom programming requests
via hello@philtel.org
Payphones can be field reprogrammed
  With permission of course

## Slide 37
Next Steps
Custom programming automation so people can request specific programming and then have it available shortly
Reverse engineering to eliminate ExpressNet entirely
  Possible integration into Asterisk softmodem
Programming lines for ElcoTel Phones and Nortel Millenniums
  We already have hardware and software for this!
Full automation of COCOT scanning software

## Slide 38
Questions?
Mike
mike@philtel.org
Famicoman (Libera IRC)
https://famicoman.com
https://github.com/Famicoman
Naveen
interlinked@philtel.org
InterLinked (Libera IRC)
https://interlinked.us
https://github.com/InterLinked1